## Slide 1: Advanced Processing for Universal Nodes
Presented by someone …

## Slide 2: A simple example: PPP(oE) and TLS/TCP tunneling
IPv4
IPv4
PPP
PPPoE
ETH
relay
session
AAA
L1
ICMP
ICMP/ARP
Transport Function
Adaptation Function
TLS
TCP
IPv6
ETH
L1
Transport Function
IPv4
PPPoE/PPP and TLS
Transport Function
TCP/IPv6
Ethernet
PEP
PDP
state
state
TLS
TCP ctl block

## Slide 3: Options for implementing advanced processing on a Universal Node
Goal: map a machine readable description of the protocol stack to the universal node (with all kind of optimizations …)
OpenFlow offers lightweight stateless processing with a memoryless property
The dom0-vswitchd is limited in its processing capabilities, but the UN offers us a rich feature set of VMs (lightweight, fully virtualized, dom0-processes) for fulfilling our processing needs …
OS a
IP
pp
OS a
IP
p
OS
App
OS
???

## Slide 4: Today‘s Solution
Application process
Problem: many heterogeneous devices exposed towards control plane, complex to program, error prone, VM is black box from UN‘s pespective 
optimal mapping not that easy to achieve
ETH
ETH
relay
OpenStack deployed VM
Ethernet flow switch
Ethernet flow switch
PPP(oE)
TLS
TCP/IP
ETH
ETH
ETH
ETH
relay
VM
dom0 vswitchd
dom0 vswitchd
Black box 

## Slide 5: Insights
Universal node exposes detailed view on its internals, granularity on VM level
VM hosts arbitrary logic  seems to be hard to map in an optimized manner to underlying physical resources
Idea: Instead of exposing the UN‘s internal details, offer a well-known interface (working assumption: SDN/OpenFlow) with enriched processing capabilities (like TLS/TCP endpoint)
Map these processing capabilities to lightweight processes (or containers like LXC containers on Linux) and route traffic towards these processing nodes automatically in the node, do not bother the control plane with such details
From the control plane‘s perspective, a single node with a powerful single data path element is offered
Btw., we do not intend to abandon the existing VM based model !!
However, we propose an extended interface to the control plane in addition!!!

## Slide 6: Back to our example: What processing needs do we have?
IPv4
IPv4
PPP
PPPoE
ETH
relay
session
AAA
L1
ICMP
ICMP/ARP
Transport Function
Adaptation Function
TLS
TCP
IPv6
ETH
L1
Transport Function
IPv4
PPPoE/PPP and TLS
Transport Function
TCP/IPv6
Ethernet
PEP
PDP
state
state
TLS
TCP ctl block

## Slide 7: PPP(oE) simple lightweight processing TLS/TCP requires complex control blocks
PPP(oE)  control state stored in controller, packet blocking using session IDs (simple matching)
TLS/TCP  session control block for connection establishment/maintenance
IPv4
IPv4
PPP
PPPoE
ETH
relay
session
AAA
L1
ICMP
ICMP/ARP
Transport Function
Adaptation Function
TLS
TCP
IPv6
ETH
L1
Transport Function
IPv4
PPPoE/PPP and TLS
Transport Function
TCP/IPv6
Ethernet
PEP
PDP
state
state
TLS
TCP ctl block

## Slide 8: Options for advanced processing extend OF dpt vs. VM
PPP(oE) can be easily integrated into the existing OF data path model  stateless processing
  Push/pop PPPoE/PPP
  Flow identification based on MAC addresses and PPPoE session Ids
  Memoryless property applies to PPP(oE)
In our example we also need a TLS/TCP endpoint
  Such endpoints require complex control blocks  put it into a VM
  TLS/TCP is a protocol layer transition which are modeled by push/pop actions in OpenFlow  new actions:
    push/pop TCP and push/pop TLS

## Slide 9: Chaining of heterogeneous processing entities
Application process
IPv4
IPv4
PPP
PPPoE
ETH
relay
ETH
PEP
TLS
TCP/IP
ETH
ETH
ETH
ETH
relay
Offers TLS/TCP processing
Offers PPP(oE) processing
Offers L2 switching
Internal login for mapping complex Flow Mods to forwarding/processing engines
Offers L2 switching, PPP(oE) and TLS/TCP processing towards control plane
OpenFlow
OpenFlow
OpenFlow
OpenFlow
VM
data path
data path

## Slide 10: Open Questions (= potential next steps)
Identify crucial actions required for building real-world protocol stacks (TCP, TLS, IPsec, …)
Is the OF action model sufficient for handling stateful processing?
  Do we need extensions (e.g. for deploying a new TCP endpoint)?
How does the Universal Node‘s internal control logic looks like for mapping complex Flow Mods towards the node‘s internal architecture?

## Slide 11
Script: [ Lonesome cowboy rides into the sunset … ]
The End
A UNIFY project release
All rights reserved